## Slide 1: Water Ratio Improvement
Nestlé Port Qasim Factory - 2020

## Slide 2
Water Ratio Improvement - PQF
Chart: Water Ratio (ton/ton) Improvement 2008-2019
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Water Ratio (ton/ton) | 5.1 | 4.1 | 2.9 | 2.68 | 2.599 | 2.2181 | 1.9686 | 1.8615 | 1.8749 | 1.6718 | 1.6266 | 1.5529
Key Water Saving Projects:
2008 – 2012: Reducing Operational losses on Fillers and Washer
2013: Detailed water map was done followed by GPI exercise
2014: Optimization of CIP, Backwash & RO flushing Sequences
2015: New 10 pre-filter + GFS tank installation
2016: Installation of Recovery RO-Saved 28 Mio Lit/annum and DMAIC on HOD Filler Losses
2017: Reduction in Retail Line Diversions via new ozone injection point and Recovery RO Water Usage in GFS tank
2018: Recovery of Water from market Returned leak bottles
2019: Increase in RO Global Recovery from 85.7% to 90% via raw water feed conductivity improvement and shifting to DDCD CIPs for backline